Solent Trifoiler Software Emulator
A load carrying foiling craft.
The main, forward, load-bearing foil is fixed. The twin rudders at the stern each have lifting foils. By varying the rake of each rudder independently the pitch and roll of the craft can be controlled. The rudders also rotate about a vertical axis to allow steering when the craft is not foiling.

The Emulator
The real world craft will have carefully designed and manufactured foils. The software model defines eleven foils in space. Each foil, rudder or strut is represented in the visualisation as a flat board, a few millimetres thick, with a black edge. Different colours are used in for the board sides order to make their orientation more obvious. The port side of the symmetric boards is coloured red. The starboard side is coloured green. The top side of the asymmetric (lifting) foils is coloured beige and the bottom is coloured blue.
In this picture, the system is pitched up by 2 degrees. The tops of the asymmetric foils are visible.
Each rudder has two lifting wings fixed at the bottom.
The pivots for the moving parts of the system are at the stern of the craft – out of the water.
The software model simply computes the forces generated by each foil and calculates their effect on the craft when applied for two milliseconds. This ‘iteration’ is carried out repeatedly.
We’re hoping that the mathematics carried out on the foils is a good approximation of what will happen in the real world. The formulas used are detailed in one of the appendices (below). If we’ve got the formulas right – and if the specified moments of inertia, the damping values and the drag values are sensible then driving this emulator should be similar to driving the real thing.
Low speed non-foiling travel is not emulated. An emulator session starts with a specified speed, ride height, direction and control settings.
Your PC updates the visual display at least ten times per second. A fast PC will update the screen more frequently. In between each update, enough iterations are carried out to catch up with the ‘virtual’ clock. In real time mode, a slow PC might need to do as many as 100 iterations to catch up. A fast PC will do fewer iterations more frequently. It should make little difference to what you see on the screen. There are several clock modes: real time, half speed, quarter speed, tenth speed and one hundredth speed. The clock mode makes no difference to the maths carried out in each iteration.
The camera follows the craft. It moves in such a way that it points, through the craft centre of gravity, in the direction that the craft is travelling. N.B. NOT the direction that the centre line of the craft is pointing (the heading). The view from the camera is orthogonal (no perspective) in order to make the orientation of the craft more obvious.
The craft body is mainly supported on the two main struts. These rise from the asymmetric main foil. The main foil has an asymmetric wing each side. The forward struts and foils are fixed – no moving parts.
In the representation, the rudders are in free space. In the real world there will be structure across the stern of the boat for them.
The asymmetric foils on the rudders also provide a small proportion of the overall lift required to keep the craft up.
Your first drive.
Visit the site and click the ‘Learner Driver’ button. This will load a set of parameters that will fire boat straight and level with enough thrust to maintain the initial speed speed. The simulation will run at one tenth speed. When you’re ready, click the ‘Start’ button. The screen switches to the model view.
Move your mouse pointer into the virtual joystick square. No need to hold down a mouse button. When your mouse pointer moves over the top of the green spot the simulation will start.
Move the mouse left/right to induce roll. Move the mouse forward/back to induce nose-down/nose-up. Increase/decrease thrust with the mouse wheel. To stop the simulation, press the escape key on your keyboard.
You can fly the boat without using the rudder but if you want to see the effect, the top row of keys on your keyboard sets the rudder.
The ‘6’ centres the rudder. The ‘5’ keys sets a degree to port. The ‘7’ key sets a degree to starboard. The ‘=’ key puts the rudder hard to starboard.
Flying straight and level
If the craft rolls, counteract the roll with a small joystick mouse movement. If you bow goes down, pull back on the joystick mouse.
Try boosting the power with your mouse wheel. Watch your speed increase. As your speed increases, more lift is generated causing the craft to rise. Push your bow down with a little forward movement of your mouse joystick.
Turning
Try maintaining a few degrees of roll to port for twenty or thirty seconds (virtual time). Note that this causes the craft to yaw and exposes the starboard side of the rudders and struts. This seems counter-intuitive at first glance but remember; the camera that is following you is pointing in the direction you are travelling. The sideways component of the asymmetric foils is pushing you to port. The camera is behind you off to your starboards side. The near-vertical asymmetric foils are actually resisting sideways movement to port a little.

Notice that your ride height falls as you turn. If you point your bow up to overcome this your speed will fall. Boost your thrust to keep your speed up.
Not that the compass points drawn on the horizon appear to be moving as you turn.

Pre-flight Starting Parameters and Control Settings.

The controls outlined in red in the picture set the vessel up for the start of the flight.
The values you set, may or may not cause a quick plunge or climb out of the water. If you’re testing, you might be expecting this and intend to study the log to see what happened. Otherwise you should consider using the ‘A’ button. It automatically sets the pitch, rudder rakes and propeller thrust for initial straight and level flight. Roll, yaw and climb will be set to zero. Ride height and knots will remain as set.

Changing the Design of the Craft

The controls outlined in red above allow you to change the design of the craft.
When you change the design of the craft, for your first flight test it might be a good idea to click the ‘A’ button. This takes into account the design changes you have made and sets up for an initial straight and level flight.
In the table below, the datum point is the centre point of the line joining the pivot points of the two rudders. For the single rudder craft it is the rudder pivot point. For the emulator, a rudder pivot point is common for rake and turn. This might not be the case for a real world craft.
The x axis is parallel to the centre line of the craft. Positive x is towards the bow.
The y axis is parallel to the beam of the craft. Positive y is towards port.
The z axis is parallel to mast of the craft. Positive z is up.
Items marked with a star are flight set-up parameters – not part of the craft design.

strutLdgEdgeX	Metres from datumX forward to strut leading edge
strutLdgEdgeBtmZ	Metres from datumZ vertically to bottom of strut leading edge. Typically this value will be negative.
strutChord	Metres main strut chord
graphicScale	Scale at which the user-supplied model data is drawn.
graphicX	Metres. Indicates where the user-supplied model data is drawn. Relative to rudder pivot point. For twin rudder craft - relative to the mid point of the line joining the two rudder pivot points.
graphicZ	Metres. Indicates where the user-supplied model data is drawn. Relative to rudder pivot point. For twin rudder craft - relative to the mid point of the line joining the two rudder pivot points.
degreesRoll	degrees. Positive is roll to port.
degreesPitch	degrees. Positive is prow up.
degreesYaw	degrees. Positive is yaw to port.
strutSep	Metres horizontally beween the main struts
mainFoilChord	Metres. Main foil chord.
mainFoilAOfA	Degrees. Angle between main foil chord and the horizontal when vessel is level. Positive is leading edge up.
kX	Moment of inertia (I = mk²) about vessel x-axis through C of G.
dampingX	Linear acceleration along fore/aft axis damping factor. (0 to 100). 0 specifies no damping.
dampingYZ	Angular roll damping factor. (0 to 100). 0 specifies no damping.
knots	knots.
newtonsPort	newtons port propeller thrust
newtonsStbd	newtons starboard propeller thrust
wingLength	Metres. Length of one main foil wing. From bottom of strut to wing tip.
wingChord	Metres main wing chord (may differ from main foil chord)
wingDihedral	Degrees. Upward angle of the wing from the horizontal, measured at the wing tips compared to the wing base.
kY	Moment of inertia (I = mk²) about vessel y-axis through C of G.
dampingY	Linear acceleration along port/stbd-axis damping factor. (0 to 100). 0 specifies no damping.
dampingZX	Angular pitch acceleration damping factor. (0 to 100). 0 specifies no damping.
metresRideHeight	Starting ride height. Metres C of G above water line
degreesElevator	Degrees rudder rake. Positive increases elevator foil angle of attack. (bow down)
degreesRudder	Degrees Rudder Angle. Positive steers to port.
rudLdgEdgeX	Metres from datumX forward to rudder leading edge
rudLdgEdgeBtmZ	Metres from datumZ vertically to rudder leading edge bottom. Typically this value is negative.
rudChord	Metres rudder blade chord
kZ	Moment of inertia (I = mk²) about vessel z-axis through C of G.
dampingZ	Linear acceleration along vessel up/down axis damping factor. (0 to 100). 0 specifies no damping.
dampingXY	Angular yaw acceleration about vessel z-axis damping factor. (0 to 100). 0 specifies no damping.
metresPerSecondClimb	metres per second - initial climb rate. Can be negative.
degreesAileron	Degrees. Increase starboard rudder rake by this value and decrease port rudder rake this value.Positive induces roll to starboard.
millisSampleTime	Milliseconds. Interval between controller updates (if PID feedback). Also interval between picture updates.
rudSep	Metres between the two rudders. Zero indicates single rudder
rudWingLength	Meters measured from the tip to where wing joins the blade. (Total rudder wing span is twice this)
rudWingChord	Metres rudder wing chord
wingAOfA	Degrees. Angle between a wing chord and the horizontal when vessel is level. Positive is leading edge up.
foilFactor	Foil drag factor. (0..1)
strutFactor	Strut drag factor. (0..1)
feedbackProportionalGain	Proportional feedback gain 0..1
feedbackIntegralGain	Inegral feedback gain 0..1
feedbackDerivativeGain	Derivative feedback gain 0..1
propellerZ	Metres from datumZ vertically to propeller centre of effort
propellerNewtons	Newtons. Maximum force generated by ONE propellor
kilogramsMass	Kilograms. Mass of Vessel.
depthMin	Depth above which the 'close to surface' effect is significant.
depthZero	Main foil above this depth has zero lift.
degreesPerSecondElevator	Elevator degrees per second max rate of change.
disturbance	Water disturbance. (0..100) Random currents, updrafts, eddies, etc. affecting the foils. Zero is none, 100 is severe.
delay	Microseconds. (0..50000) Delay the application of PID corrections.
cOfGX	Metres. Indicates where centre of gravity of the craft is - relative to the rudder pivot point. For twin rudder craft, relative to the mid point of the line joining the two rudder pivot points. Positive x is forward.
cOfGY	Metres. Indicates where centre of gravity of the craft is - relative to the rudder pivot point. For twin rudder craft, relative to the mid point of the line joining the two rudder pivot points. Positive y is to port.
cOfGZ	Metres. Indicates where centre of gravity of the craft is - relative to the rudder pivot point. For twin rudder craft, relative to the mid point of the line joining the two rudder pivot points. Positive z is up.
rakeMax	Degrees. Maximum rudder rake.
aileronMax	Degrees. Maximum aileron value. Port/stbd rudder rake difference to cause roll.

Autopilot
Automatic ride height control is a desired feature for a real world craft.
The main design feature of the craft (controlled by rudder rake - no moving parts under water) presents some control difficulties. Here’s the possible explanation.
- To control the ride height, the angle of attack of the main foil needs to be controlled. Because the main foil is fixed, the whole craft needs to be rotated to change the angle of attack.
- The craft has a significantly large moment of inertia so the rudder foils have to do work to get the vessel rotating in the vertical plane.
- Unfortunately, when the desired main foil angle of attack has been achieved, the vessel will continue rotate because of it's inertia.
- A change to the elevator angle will need to be applied and do more work to reduce reduce the rate of rotation to zero.
- In the meantime, the angle of attack will continue to change, so, somehow, the second change will need to be calculated and applied before the desired new angle of attack is reached.
Emulator PID controller tests taking as input the ride height were found to be unsuccessful. It’s not proved but it’s possible that the nature of the control (outlined above) makes direct PID control of ride height impossible.
It turns out though, that PID control of the rate of the emulated craft’s change of pitch can be successful. It’s reasonably easy to find PID values that work to maintain a constant rate of change of pitch; set the craft flying straight and level and it will continue flying straight and level; set it flying with a non-zero rate of change of pitch (describing an arc) and it will continue to describe the same arc.
When you set any of the PID controls to non-zero, the behaviour of the model changes. Forward and backward movement of the mouse joystick increases the set point of the PID controller. When the joystick is centred, the rate of change of pitch is controlled to zero.
Controlling the rate of change of pitch is not a complete solution but it’s a step on the way towards developing an overall autopilot.
The PID values you need will depend on your design. For all three PID controls, zero is no feedback, a value of 1 is the maximum. Search the internet for pages giving advice on setting PID controls. Oscillation is hard to see on the screen; you’ll need to look at the log to see what’s happening.
PID corrections are calculated and applied at the end of every sample period.
Before each test flight, set the disturbance value. This causes random changes in the water (cross-currents, eddies, up-drafts and down-drafts). A value of 100 is severe. A value of zero requests total calm but the finite nature of the computer numbers used in the calculations will introduce very small disturbances.
In the emulator, sensor values are simply the currently calculated values. In a real world craft these values will come from the onboard sensors. At the current time, it’s not known whether or not the sensors available are accurate enough and fast enough to control a real world craft.
If you know that the PID system on your proposed real world craft will introduce a delay, you can emulate it in the flight settings. The delay value unit is microseconds.

Appendix A. Foil Calculations.
The emulator treats a foil as a rectangle in 3-dimensional space. The following properties are maintained for each foil.
- The four corners.
- The centre of pressure
- foil.metresParentFoilSpan
foil.metresParentFoilSpan is a property of asymmetric foils. It is the total span of the other asymmetric foils to which it is joined.
Each iteration calculates the force generated by each foil as it moves through the water.
Asymmetric Foils
Here is the pseudo code that is carried out for each asymmetric foil during an iteration.
The water is assumed to be stationary. The foil is assumed to be moving through the water.
The centre of pressure point is calculated.
Foil.velocityVector is calculated as the difference between the current centre of pressure and the previous centre of pressure divided by the iteration time.
N.B. The iterator stores the old centre of pressure position before it updates with the new one.
foil.degreesAngleOfAttack is calculated using the foil corners and the foil velocity vector.
twoDLiftCoeff is calculated as 0.11 * (4 + foil.degreesAngleOfAttack)
aspectRatio is calculated as foil.metresParentFoilSpan / foil.metresChord
threeDLiftCoeff is calculated as twoDLiftCoeff / (1 + (3 / aspectRatio));
inducedDragCoeff is calculated as threeDLiftCoeff * threeDLiftCoeff / (Math.PI * aspectRatio);
metresPerSecond is calculated from foil.velocityVector
inducedDrag is calculated as 0.5 * Forces.seaWaterDensity * (foil.area) * metresPerSecond * metresPerSecond * inducedDragCoeff;
threeDLift is calculated as 0.5 * Forces.seaWaterDensity * (foil.area) * metresPerSecond * metresPerSecond * threeDLiftCoeff;
twoDPressureDragCoeff is interpolated from the lookup table below.
twoDPressureDrag is calculated as 0.5 * Forces.seaWaterDensity * (foil.area) * metresPerSecond * metresPerSecond * twoDPressureDragCoeff;
foil.liftDirectionVector is calculated to be the unit vector that is perpendicular to velocity of the foil centre of pressure and in a plane that contains the velocity vector and a vector that is normal to the plane of the foil.
Foil.liftVector is calculated by multiplying foil.liftDirectionVector by threeDLift.
foil.ldragDirectionVector is calculated to be the inverse of the unit vector that is parallel to foil.velocityVector.
TotalDrag is calculated as inducedDrag + twoDPressureDrag;
Foil.liftVector is calculated by multiplying foil.liftDirectionVector by threeDLift.
Foil.dragVector is calculated by multiplying foil.dragDirectionVector by totalDrag.